Host A
Host B
block 10.1.9.16/28
block 10.1.9.32/28
endpoint
10.1.9.17
endpoint
10.1.9.33
endpoint
10.1.9.18
Routes:
10.1.9.32/28 → Host B
Routes:
10.1.9.16/28 → Host A
Figure 1: Blocks, endpoints and routes in the cluster after creation of the third endpoint

---
core
Only routes for prefix groups need to be announced to core routers
routes:	10.1.0.0/10 → ToR-1
10.1.64.0/10 → ToR-2
Rack 1: L2 domain
Rack 2: L2 domain
ToR-1
ToR-2
routes	10.1.1.16/28 → Host A
10.1.4.64/28 → Host A
10.1.0.16/28 → Host B
default → core
routes	10.1.64.32/28 → Host C
10.1.64.16/28 → Host D
ToRs have routes to all address blocks within the L2 domain
Host C
block 10.1.1.16/28
block 10.1.64.32/28
block 10.1.4.64/28
routes	10.1.0.16/28 → Host B
default → ToR-1
routes	10.1.64.16/28 → Host D
default → ToR-2
Hosts have routes to all blocks in L2 domain, plus default route to ToR
Host D
block 10.1.0.16/28
block 10.1.64.16/28
default → ToR-1
default → ToR-2
Figure 2: Romana blocks and routes in an 'L2-to-the-host' data center

---
Every host is in its own network segment
routes	default → ToR-2
routes	default → ToR-1
Hosts only need default route to ToR
routes	default → ToR-2
routes	default → ToR-1
Figure 3: Romana blocks and routes in an 'L3-to-the-host' data center